## Slide 1
SOH · RUL
SCOPE · B.TECH PROJECT
Adaptive Physics-Informed Battery Digital Twin for SOH and RUL Prediction
Energy AI · Battery Management Systems · Physics-Informed Neural Networks
TEAM
M. Chethan Krishna 23BAI0093
K. Shanmukha Santhosh 23BAI0157
Ashok Reddy 23BAI0143

## Slide 2
DOMAIN & MOTIVATION
Project Overview & Use Cases
DOMAIN
Energy AI · Battery Management Systems
TYPE OF DNN
Physics-Informed Neural Network (PINN) + Feedforward DNN
THE CHALLENGE
Li-ion batteries degrade with cycling, temperature and age. Pure deep-learning models need large labeled datasets and can be physically inconsistent; pure physics models are too slow for real-time use.
OUR APPROACH
An Adaptive PINN Battery Digital Twin fuses PINNs, a Transformer Encoder and Incremental Adaptive Learning to continuously estimate SOH and RUL — adapting to new data without full retraining.
WHERE IT APPLIES
Use Case | Impact
Electric Vehicles | Tesla, BYD, Hyundai, Tata EV, MG — predict battery replacement before failure
Battery Swapping Stations | Identify which battery packs should be retired
Solar Energy Storage | Monitor home batteries and predict maintenance
Grid-Scale Storage | Avoid sudden, unplanned battery failures
Drone Batteries | Estimate safe remaining flying time
Space Missions | Battery swaps are impossible — lifetime prediction is critical
Smartphones & Laptops | Sharper degradation estimates than today's health meters
Adaptive PINN Battery Digital Twin
2 / 10

## Slide 3
MOTIVATION
Problem Statement
Lithium-ion batteries power electric vehicles and renewable energy storage, but their performance degrades with charge cycles, temperature, current load and age. Accurately estimating State of Health (SOH) and Remaining Useful Life (RUL) is essential for safety, reliability and efficient maintenance.
Deep Learning Models
Require large volumes of labeled training data
May produce physically inconsistent predictions
Limited generalization to unseen operating conditions
Physics-Based Models
Computationally expensive to run
Difficult to deploy for real-time estimation
Rely on complex electrochemical simulations
Adaptive PINN Battery Digital Twin
3 / 10

## Slide 4
SYSTEM DESIGN
Proposed Approach & Architecture
Real-time sensor data, electrochemical battery physics and deep learning combine to estimate SOH and RUL. The Digital Twin continuously adapts to new battery behaviour through incremental learning — no full retraining required.
1
Historical Battery Dataset
Voltage, current, temperature and cycling history feed the pipeline.
2
Transformer Encoder
Learns long-term degradation patterns across sensor streams.
3
PINN Layer
Embeds electrochemical physics so outputs stay physically consistent.
4
Feedforward NN
Produces final SOH and RUL predictions.
5
Adaptive Learning Module
Detects behaviour shifts and updates the twin incrementally.
Adaptive PINN Battery Digital Twin
4 / 10

## Slide 5
FOUNDATION REFERENCE
Base Paper
Physics-Informed Neural Networks for Battery Modeling and State Estimation: A Methodological Review
Renewable and Sustainable Energy Reviews, 2026
WHY THIS PAPER WAS SELECTED
Comprehensive review of Physics-Informed Neural Networks (PINNs) for battery applications
Covers SOH, RUL, SOC, Digital Twins, thermal diagnosis and internal state reconstruction
Explains multiple methods for embedding battery physics into neural networks
Discusses training stability, domain generalization, uncertainty quantification and interpretability
Lays out future research directions for intelligent Battery Management Systems
Adaptive PINN Battery Digital Twin
5 / 10

## Slide 6
POSITIONING OUR WORK
Literature Review & Research Gap
RESEARCH GAP
Existing PINN models are trained offline, adapt poorly to changing battery behaviour, and remain difficult to deploy in real-time BMS. Lightweight, continual-learning methods are still an open problem.
Paper | Key Contribution | Limitation | Our Improvement
Applied Energy (2025) | PINN + Transformer + multi-task learning predicts SOH, RUL and degradation path | Offline training; adapting to new behaviour needs retraining | Adaptive Digital Twin with incremental fine-tuning
Energy (2026) | EM-PINN integrates SEI growth physics for accurate SOH estimation | SOH-only; no Digital Twin or continual adaptation | Combines PINN with a Digital Twin predicting SOH and RUL
Scientific Reports (2025) | Cycle-aware physics-informed framework for RUL prediction | Offline; limited personalization per battery | Continuously updates predictions with new operational data
Complex & Intelligent Systems (2025) | PINN + contrastive learning for low-label SOH estimation | Train-then-deploy workflow; no post-deployment adaptation | Supports incremental learning without full retraining
Proposed Work | Transformer + PINN + Feedforward DNN + Digital Twin + Adaptive Learning | — | Incremental fine-tuning on new battery behaviour, preserving physics constraints
Adaptive PINN Battery Digital Twin
6 / 10

## Slide 7
FOUNDATION FOR TRAINING
Datasets Used & Rationale
SELECTED DATASETS
Public benchmark battery datasets cited across the reviewed papers, spanning lab-aged, second-life, and vehicle-field conditions, chosen to validate SOH/RUL estimation under diverse chemistries and operating regimes.
Dataset | Scope | Link | Why This Dataset
NASA & Oxford Battery | Lab-aged Li-ion cells; narrow current/temperature range; classic PINN-SOH benchmark | data.nasa.gov (PCoE) / howey-lab Oxford Battery Degradation Dataset | [0] Standard reference set used by our base-paper PINN methodology review to validate degradation-physics constraints
Stanford-MIT-Toyota (Severson) | 124 LFP/graphite cells, 72 fast-charging policies, cycled to end-of-life | data.matr.io (Battery Evaluation and Early Prediction project) | [1] Used by the RUL-focused papers for early-cycle degradation trajectories and fast-charging diversity
TJU & XJTU | Multi-chemistry aging data with IC-curve health features across varied cycling protocols | Tianjin University / Xi'an Jiaotong University battery aging repositories | [2] Referenced by the time-series PINN-SOH literature to test cross-dataset transfer of the Adaptive Learning module
CALCE & Panasonic 18650PF | Dynamic charge/discharge cycles, -10°C to 20°C, multi-temperature conditions | calce.umd.edu (Battery Research Group) / NASA Ames Prognostics Center | [3] Provides low-temperature, condition-diverse cycles to stress-test physics-informed robustness
Second-Life LIB (SL-LIB) | 84 retired batteries, 21 working conditions, real second-life usage patterns | Self-designed dataset (Bayesian PINN, Applied Energy 2025) | [4] Real-world retired-battery data supports validating adaptive learning on genuinely shifting degradation behaviour
Datasets Used & Rationale
7 / 11

## Slide 8
WHAT SETS THIS WORK APART
Novel Contribution: Adaptive Incremental Learning
Traditional models are trained once on historical data. When battery behaviour shifts with aging, temperature or charging patterns, the whole model must often be retrained — expensive and impractical for real-time BMS.
WITHOUT ADAPTIVE LEARNING
Old + New
Dataset
Retrain
Everything
Deploy New
Model
WITH ADAPTIVE LEARNING (PROPOSED)
Existing Model
+ New Data
Fine-Tune
Only
Updated
Model
HOW IT WORKS
1
Monitor real-time sensor data (V, I, temperature, SOC, cycle count)
2
Detect changes in degradation behaviour
3
Store important new data in a replay buffer
4
Incrementally fine-tune the existing model
5
Update the Digital Twin — no full retraining
ADVANTAGES
Eliminates full model retraining
Adapts to changing battery behaviour
Personalized prediction per battery
Physics-consistent predictions via PINN
Fit for real-time BMS deployment
Adaptive PINN Battery Digital Twin
8 / 11

## Slide 9
REAL-WORLD IMPACT
Applications
1
Electric Vehicles
Predict battery replacement before failure occurs.
2
Solar Storage
Monitor home batteries and predict maintenance needs.
3
Smart Grids
Avoid sudden, costly battery failures at scale.
4
Drones
Estimate safe remaining flying time in-flight.
5
Laptops & Smartphones
More accurate battery degradation estimates.
Adaptive PINN Battery Digital Twin
9 / 11

## Slide 10
CONCLUSION
Project Summary
Proposed an Adaptive Physics-Informed Battery Digital Twin for accurate SOH and RUL estimation.
Integrated Transformer Encoder, PINN and Feedforward DNN to combine data-driven learning with battery physics.
Introduced incremental adaptive learning to keep the Digital Twin current without full model retraining.
Overcomes key limits of pure deep-learning and pure physics-based models with real-time, physically consistent predictions.
Potential impact: Electric Vehicles, Battery Management Systems, Renewable Energy Storage, Smart Grids, Drones and Consumer Electronics.
Adaptive PINN Battery Digital Twin
10 / 11
Adaptive PINN Battery Digital Twin
9 / 10

## Slide 11
SOURCES
References
1
Physics-informed neural networks for battery modeling and state estimation: A methodological review
Renewable and Sustainable Energy Reviews, 2026 https://www.sciencedirect.com/science/article/pii/S1364032126005253
2
Physics-informed neural network for co-estimation of state of health, remaining useful life, and short-term degradation path in Lithium-ion batteries
Applied Energy, 2025 https://www.sciencedirect.com/science/article/pii/S0306261925011572
3
Physical informed neural network for SOH estimation of Lithium-ion battery with electrochemical mechanism
Energy, 2026 https://www.sciencedirect.com/science/article/pii/S0360544225053964
4
A cycle-aware and physics-informed framework for battery remaining useful life prediction
Scientific Reports, 2025 https://www.researchgate.net/publication/399255851_A_cycle-aware_and_physics-informed_framework_for_battery_remaining_useful_life_prediction
5
Physics-informed neural network and momentum contrastive learning for battery state of health estimation
Complex & Intelligent Systems, 2025 https://www.researchgate.net/publication/398786756_Physics-informed_neural_network_and_momentum_contrastive_learning_for_battery_state_of_health_estimation
Adaptive PINN Battery Digital Twin
11 / 11

## Slide 12
PHASE II · REVIEW 2
Model Design & Experimental Study
Completed implementation, experimental evaluation, and benchmark analysis
NASA-first evidence bundle
54 hyperparameter combinations · 3 random seeds · 18 ablation rows · 12 robustness rows
Key Evaluation Focus
Model architecture · Multiple models · Hyperparameter tuning · Experimental analysis · Methodology & Development Summary
Adaptive PINN Battery Digital Twin
12 / 21
Notes: Phase II section appended to the supplied deck. Evidence source: D:/DL/battery_twin/outputs/final_evidence_v2/evidence_results.json.

## Slide 13
PHASE II · DELIVERABLE
Phase II focus: DL model design and hyperparameter tuning
The required work is explicit: design the DL models, tune their hyperparameters, deploy multiple models, and compare results.
1
Data contract
NASA B0005, B0006, B0007, and B0018 are parsed into ordered discharge-cycle records with voltage, current, temperature, time-gap, and capacity.
2
Model stack
DNN, GRU, Transformer-only, PINN, and adaptive Transformer-plus-physics models run under the same held-out-cell protocol.
3
Online learning
A drift detector triggers low-cost replay-buffer updates as the held-out stream arrives in time order.
4
Experimental Evidence
The run exports final comparison tables, ablations, robustness results, physical diagnostics, figures, and a reflection script.
5
Scope & Boundary
SEI-PDE physics and broad multi-chemistry validation remain extensions because the NASA POC does not expose every required electrochemical variable.
6
Experimental Rigor
Reported paper metrics stay separate from new project metrics. The project claims only what the executed protocol measures.
Adaptive PINN Battery Digital Twin
13 / 21
Notes: Project implementation files: D:/DL/battery_twin/src/battery_twin and D:/DL/battery_twin/scripts. The source audit in the HTML report distinguishes proposal claims, literature evidence, and new student evidence.

## Slide 14
PHASE II · DATASET
NASA cells and a leakage-safe evaluation protocol
The official NASA PCoE repository provides the first committed dataset for this proof of concept.
Item | Project choice | Why it matters
Cells | B0005 / B0006 / B0007 train · B0018 held out | Battery-level separation tests transfer to a new cell.
Labels | SOH = capacity / nominal capacity × 100 · EOL = 70% SOH | RUL = EOL cycle − current cycle.
Inputs | Voltage · current · temperature · delta_t · cycle index | Measured timing is retained with masks.
Protocol | 504 train windows · 132 test windows · 33 initial · 99 stream | Later cycles arrive sequentially for adaptation.
Seeds | 7 · 17 · 27 | Final tables report mean ± standard deviation.
EOL RULE
70% SOH
HELD-OUT CELL
B0018
CYCLES PARSED
636 total
ORDER
Time-aware
METRIC UNIT
RUL in cycles
Adaptive PINN Battery Digital Twin
14 / 21
Notes: Dataset source: https://www.nasa.gov/intelligent-systems-division/discovery-and-systems-health/pcoe/pcoe-data-set-repository/. Local audit and labels are implemented in data.py and features.py. The 636-cycle count is the parser audit across the four selected NASA files.

## Slide 15
PHASE II · ARCHITECTURE
From measured cycle to adaptive digital-twin state
The first-stage physics model uses relationships supported by the NASA measurements.
•
NASA records
Cycle-level voltage, current, temperature, time, capacity
•
Masked encoder
Measured points + delta_t, no blind interpolation
•
Temporal model
History across cycles with Transformer context
•
SOH / RUL heads
Bounded SOH 0–100 and non-negative RUL
•
Physics losses
Soft degradation, RUL order, capacity-curve residual
•
Replay adaptation
Drift trigger, recent + representative history
Training objective
L_total = L_data + λ_phys L_phys + λ_cons L_cons
The SEI-growth PDE formulation remains a Stage 2 extension until every variable and parameter is available and verified.
Adaptive PINN Battery Digital Twin
15 / 21
Notes: Implementation sources: models.py, physics.py, training.py. The methodology review and EM-PINN paper inform the physics discussion, but the student POC does not claim to reproduce the SEI-PDE experiment.

## Slide 16
PHASE II · TUNING
The selected configuration came from the complete grid
Every requested combination ran across seeds 7, 17, and 27 before the final evidence pass.
Grid dimension | Values tested
Hidden size | 64 · 128
Learning rate | 0.0001 · 0.0005 · 0.001
Physics weight | 0.1 · 1 · 10
Replay size | 128 · 512 · 2048
Total combinations | 54 × 3 seeds = 162 runs
Selected configuration
Hidden size 64
Learning rate 0.001
Physics weight 0.1
Replay size 128
The final evidence runner then used the selected configuration on the full default cycle-window representation.
GRID STATUS
54 / 54 complete
MODEL COUNT
5 comparisons
EVIDENCE MODE
Held-out cell
OUTPUT
JSON + CSV + PNG
Adaptive PINN Battery Digital Twin
16 / 21
Notes: Tuning source: D:/DL/battery_twin/outputs/tuning/grid.json. The grid JSON records combinations_requested = 54, combinations_run = 54, and seeds = [7, 17, 27].

## Slide 17
PHASE II · MODEL COMPARISON
The standalone PINN led frozen SOH accuracy
All model rows use the same B0018 held-out evaluation protocol and four training epochs.
Model | SOH MAE | RUL MAE (cycles) | SOH R²
DNN | 11.05 ± 0.25 | 37.04 ± 6.18 | -6.43
GRU | 10.52 ± 1.03 | 36.39 ± 4.95 | -1.87
Transformer-only | 11.50 ± 0.56 | 43.98 ± 9.94 | -6.57
PINN without adaptation | 7.76 ± 1.42 | 38.15 ± 4.59 | -3.86
Adaptive twin | 10.05 ± 1.46 | 38.36 ± 3.39 | -4.48
Adaptive twin
10.05 ± 1.46 SOH MAE · 38.36 ± 3.39 RUL MAE
Best frozen SOH row
PINN: 7.76 ± 1.42 SOH MAE
Adaptive PINN Battery Digital Twin
17 / 21
Notes: Metrics source: D:/DL/battery_twin/outputs/final_evidence_v2/evidence_results.json and final_summary.csv. Paper metrics are not numerically ranked against this table because datasets, splits, labels, and metric scales differ.

## Slide 18
PHASE II · ABLATIONS
Replay adaptation delivered the low-cost online update
The ablation table shows which components mattered in the ordered B0018 stream.
Variant | Post-shift SOH MAE | Improvement | Work | Events
Proposed adaptive | 1.74 | 80.63% | 8.75% | 7
No physics | 1.23 | 86.98% | 8.75% | 7
No Transformer | 4.09 | 50.39% | 8.75% | 7
No replay | 3.97 | 53.23% | 8.75% | 7
No drift detection | 1.59 | 81.91% | 15.00% | 12
Full retraining | 1.58 | Reference | 100.00% | —
TARGET 1
80.63% improvement
TARGET 2
8.75% work
TARGET 3
−10.20% forgetting
DETECTOR
7 updates / seed
Adaptive PINN Battery Digital Twin
18 / 21
Notes: Ablation source: evidence_results.json and ablation_summary.csv. Negative forgetting means the initial-domain SOH MAE improved after adaptation. Full retraining is the cost reference.

## Slide 19
PHASE II · ROBUSTNESS
The adaptive state remained useful under sensor corruption
Robustness scenarios use the same trained proposal and corrupt the ordered stream before adaptation.
Scenario | Frozen SOH MAE | Adaptive SOH MAE | Updates
Clean ordered stream | 8.81 | 1.73 | 7
Voltage/current/temp noise | 9.02 | 1.52 | 7
10% missing samples | 8.78 | 1.51 | 7
Sensor drift | 8.88 | 1.69 | 7
Diagnostic | Mean ± SD
SOH bounds violations | 0.00%
Negative RUL | 0.00%
SOH degradation violation | 21.43%
SOH/RUL consistency violation | 30.95%
Capacity-curve residual | 0.00573
Interpretation
Hard bounds stayed at zero. Soft monotonic diagnostics stayed nonzero, so the result supports a measured proof of concept with calibration limits rather than perfect electrochemical validity.
Adaptive PINN Battery Digital Twin
19 / 21
Notes: Robustness and physical-validity source: evidence_results.json. The monotonic rates are diagnostics because real cells can show local capacity regeneration. Capacity-curve residual is the first-stage data-supported residual, not an SEI-PDE residual.

## Slide 20
PHASE II · FACULTY EVIDENCE
Proof of experiment mapped to the course rubric
The deck now points to concrete artifacts a reviewer can inspect.
Rubric criterion | What to show | Artifact
Model architecture design | Data → masked encoder → temporal model → physics losses → heads → replay update | HTML report · Section 05
Multiple models | DNN, GRU, Transformer-only, PINN, adaptive twin | final_summary.csv
Hyperparameter tuning | 54 combinations across three seeds | tuning/grid.json
Experimental analysis | Ablations, robustness, physical checks, acceptance table | evidence_results.json + PNG figures
Presentation and reflection | 6-minute walkthrough and AI pair-programming reflection | video_reflection_script.md
Recording checklist
Show the design diagram · show all five models · open the 54-combination grid · show one ablation and one robustness figure · read PASS status exactly
Adaptive PINN Battery Digital Twin
20 / 21
Notes: Faculty rubric source: D:/DL/RUBRICS FOR COURSE BASED DESIGN PROJECT - FALL 26-27.pdf and the supplied Phase II screenshots. The actual recording must be made and uploaded by the student; this slide and video_reflection_script.md prepare the evidence.

## Slide 21
PHASE II · FINAL STATUS
A tested adaptive POC with a clear next experiment
The strongest evidence is the low-cost online update. The main limitation is the small four-cell dataset.
What the run supports
1
Adaptation benefit
80.63% lower post-shift SOH MAE than frozen.
2
Low update cost
8.75% of full-retraining work.
What the run does not prove
• Universal chemistry or temperature generalization
• Perfect monotonic degradation behavior
• SEI-PDE validity without additional variables
• A direct numerical ranking against the four papers
Next experiment
Calibrate physics weights, add longer training, and repeat leave-one-cell-out validation before making a broader scientific claim.
Adaptive PINN Battery Digital Twin
21 / 21
Notes: Closing reflection: AI helped translate the proposal and rubric into code, tests, and evidence tables. Human scientific judgment kept unsupported SEI-PDE claims out of the first NASA implementation. Manual video recording remains the only presentation step not automated here.

## Slide 22
PHASE II · PRESENTATION
Video demonstration
Empty submission slide for the Moodle, Stream, or Drive video link
VIDEO LINK
PASTE VIDEO URL HERE
Replace this placeholder with the actual uploaded video URL before submitting.
No external video URL was present in the supplied files, so this slide intentionally keeps the link field open.
Adaptive PINN Battery Digital Twin
22 / 22
Notes: Before faculty submission, replace PASTE VIDEO URL HERE with the actual Moodle, Stream, Drive, or other approved video URL. The user did not provide a video URL in the request.

## Slide 23
PHASE II · FORMULA AUDIT
Equations used in our NASA prototype
These are the target definitions and input contract that are active in the first reproducible implementation.
STATE OF HEALTH
SOHₖ = 100 × Cₖ / C_nom
Measured discharge capacity Cₖ becomes the supervised health label. Capacity is not fed as a future deployment input.
REMAINING USEFUL LIFE
RULₖ = k_EOL − k
RUL is measured in discharge cycles remaining from the current cycle k.
END OF LIFE
k_EOL = min{k : SOHₖ ≤ 70%}
Primary project threshold. Every RUL result is interpreted against this declared EOL rule.
DEPLOYED INPUT VECTOR
xₖ = [V, I, T, Δt, k]
Voltage, current, temperature, measured time-gap, and cycle index. Irregular timing is preserved with Δt and masks.
Status: implemented and evaluated on NASA B0005/B0006/B0007 → B0018
Adaptive PINN Battery Digital Twin
23 / 31
Notes: Implementation source: D:/DL/battery_twin/src/battery_twin/data.py, features.py, models.py, and metrics.py. The EOL threshold is the student-selected primary POC rule, not a universal battery standard.

## Slide 24
PHASE II · FORMULA AUDIT
The active training objective and physical diagnostics
The first-stage POC uses capacity/degradation consistency that the NASA records can support; it does not claim an SEI-PDE residual.
L_total = L_data + λ_phys L_phys + λ_cons L_cons
selected: λ_phys = 0.1 · λ_cons = 1 · RUL scale = 250 cycles
DATA LOSS
L_data = mean|ŝoh−soh| + mean|r̂ul−rul|/250
Joint SOH and RUL regression with valid-cycle masks.
SOFT PHYSICS LOSS
L_phys = mean ReLU(Δŝoh) + mean ReLU(Δr̂ul)
Penalizes predicted SOH or RUL increases across ordered cycles; soft because real cells can show local regeneration.
CURVE CONSISTENCY
L_cons = mean|Δŝoh−Δsoh| / 100
Capacity-curve shape residual between predicted and measured SOH changes.
BOUNDED HEADS
ŝoh = 100·σ(z₁), r̂ul = 250·σ(z₂)
Output contract: SOH ∈ [0,100] and RUL ∈ [0,250]. The nonnegative-consistency term is an explicit zero-valued future hook.
Diagnostics reported: SOH bounds violation · negative RUL rate · degradation violation rate · SOH/RUL consistency violation · capacity-curve residual
Adaptive PINN Battery Digital Twin
24 / 31
Notes: Exact implementation source: D:/DL/battery_twin/src/battery_twin/physics.py and metrics.py. `nonnegative_consistency` is deliberately zero-valued because the bounded output head already enforces SOH bounds; it is not presented as an active extra constraint.

## Slide 25
BASE PAPER · EQUATIONS (1–5)
Base paper: general PINN formulation
Transcribed from the methodological review, pp. 4–5. These are representative framework equations, not one new end-to-end model.
(1) NEURAL APPROXIMATION
uθ(x,t) = NNθ(x,t)
A network represents a battery state variable such as concentration, voltage, temperature, or SOC.
(2) GOVERNING OPERATOR
𝒩[uθ](x,t; λ) = 0
𝒩 is the physical operator derived from electrochemical, ECM, aging, or thermal equations; λ denotes physical parameters.
(3) RESIDUAL
rθ(x,t) = 𝒩[uθ](x,t; λ)
Automatic differentiation evaluates the physical-law residual at a point.
(4) PHYSICS LOSS
L_phys = (1/Nₚ) Σ |rθ(xᵢ,tᵢ)|²
Residuals are averaged over Nₚ physics collocation points.
(5) COMPOSITE PINN LOSS
L_PINN = w_d L_data + w_p L_phys + w_b L_BC/IC + w_r L_reg
Weights balance data fit, governing physics, boundary/initial conditions, and optional regularization.
Implementation: We specialize data loss, physical monotonicity, and capacity curve residual losses for battery health tracking.
Adaptive PINN Battery Digital Twin
25 / 31
Notes: Source: D:/DL/0.base_paper.pdf, pp. 4–5, equations (1)–(5). The review presents this as a general methodological foundation and surveys different implementations.

## Slide 26
BASE PAPER · EQUATIONS (6–9)
Base paper: electrochemical constraints
These equations are reviewed as physics sources for PINNs; they are not activated in the first NASA POC because the required internal variables are not observed.
(6) SOLID-PHASE DIFFUSION
∂cₛ/∂t = (Dₛ/r²) ∂/∂r (r² ∂cₛ/∂r)
Fick-type diffusion in a spherical active-material particle; cₛ is concentration and Dₛ is solid-phase diffusivity.
(7) PARTICLE BOUNDARY CONDITIONS
∂cₛ/∂r|₀ = 0, −Dₛ∂cₛ/∂r|Rₛ = Jₙ
Symmetry at the particle center and surface-flux condition at radius Rₛ.
(8) BUTLER–VOLMER KINETICS
jₙ = i₀[exp(αₐFη/RT) − exp(−α𝚌Fη/RT)]
Interfacial reaction-current relation; i₀ is exchange current density and η is overpotential.
(9) CHARGE CONSERVATION
∇·iₛ = −aₛjₙ, ∇·iₑ = aₛjₙ
Solid/electrolyte current-density balance with specific interfacial area aₛ.
Electrochemical PDE Context
Reviewed for Stage 2 extension only · not claimed as an executed SEI/electrochemical experiment
Adaptive PINN Battery Digital Twin
26 / 31
Notes: Source: D:/DL/0.base_paper.pdf, p. 5, equations (6)–(9). The review explicitly discusses diffusion, boundary conditions, Butler–Volmer kinetics, and charge conservation as candidate electrochemical constraints.

## Slide 27
BASE PAPER · EQUATIONS (10–16)
Base paper: ECM state evolution and aging laws
These equations connect macroscopic circuit state, capacity fade, and monotonic degradation constraints.
(10) COULOMB COUNTING
dz/dt = −ηI(t)/Qₙ
z is SOC, I is applied current, Qₙ is nominal capacity, and η is Coulombic efficiency.
(11) RC POLARIZATION
dVₚ/dt = −Vₚ/(RₚCₚ) + I/Cₚ
First-order equivalent-circuit polarization branch.
(12) TERMINAL VOLTAGE
Vₜ = U_OC(z) − IR₀ − Vₚ
Open-circuit voltage plus ohmic and polarization terms.
(13) CAPACITY-BASED SOH
SOH(k) = Q(k)/Q₀
The base review’s capacity-health equation is the source for our percentage form SOHₖ = 100Qₖ/Q_nom.
(14–15) CAPACITY FADE
Q(k)=Q₀−ΔQ(k) or Q(k)=Q₀−akᵇ
General accumulated loss and a semi-empirical cycle-dependent approximation.
(16) MONOTONIC AGING
dQ/dk ≤ 0 or Q(k+1) ≤ Q(k)
The basis for soft degradation constraints; local regeneration can motivate a soft rather than hard penalty.
Implementation: We adopt capacity-derived SOH and soft monotonicity constraints to reflect degradation physics.
Adaptive PINN Battery Digital Twin
27 / 31
Notes: Source: D:/DL/0.base_paper.pdf, pp. 7–8, equations (10)–(16). Equation (13) directly motivates the project SOH label; equations (10)–(12) and (14)–(16) are reviewed physical formulations and constraints.

## Slide 28
BASE PAPER · EQUATIONS (17–19)
Base paper: thermal and reaction-rate constraints
The review extends the PINN equation map to coupled thermal fields and temperature-dependent kinetics.
(17) LUMPED THERMAL MODEL
C_th dT/dt = Q_gen − hAₛ(T−T_amb)
Cell temperature T evolves from heat generation, convection, and ambient temperature.
(18) DISTRIBUTED HEAT CONDUCTION
ρcₚ ∂T/∂t = ∇·(k_th∇T) + q_gen
Spatial thermal field equation with density ρ, heat capacity cₚ, and conductivity k_th.
(19) ARRHENIUS REACTION RATE
k_rxn(T) = A_r exp(−E_a/(R_gT))
Temperature-dependent reaction-rate constant with activation energy E_a.
Data Scope & Verification
The NASA cycle records expose voltage, current, temperature, time, and capacity, but not every internal concentration, flux, heat-source, or reaction parameter required to claim these residuals.
Core Physical Scope
Equations (1)–(19) are the review’s core numbered map; only measurable capacity/degradation constraints are active in our Stage 1 implementation.
Adaptive PINN Battery Digital Twin
28 / 31
Notes: Source: D:/DL/0.base_paper.pdf, p. 8, equations (17)–(19). The review is methodological; the student project deliberately postpones thermal-PDE and reaction-rate residuals until the required variables and parameters are available.

## Slide 29
PHASE II · FINAL RESULTS
Measured model comparison under the held-out-cell protocol
Mean ± standard deviation over seeds 7, 17, and 27; B0005/B0006/B0007 train and B0018 held out.
Model | SOH MAE | SOH RMSE | SOH MAPE | SOH R² | RUL MAE (cycles)
DNN | 11.05 ± 0.25 | 21.03 ± 0.08 | 13.74 ± 0.36% | -6.43 | 37.04 ± 6.18
GRU | 10.52 ± 1.03 | 13.05 ± 0.63 | 13.69 ± 1.46% | -1.87 | 36.39 ± 4.95
Transformer-only | 11.50 ± 0.56 | 21.22 ± 0.31 | 14.42 ± 0.83% | -6.57 | 43.98 ± 9.94
PINN without adaptation | 7.76 ± 1.42 | 15.81 ± 6.27 | 9.65 ± 1.53% | -3.86 | 38.15 ± 4.59
Adaptive twin | 10.05 ± 1.46 | 17.22 ± 5.45 | 12.82 ± 1.78% | -4.48 | 38.36 ± 3.39
Readout
Standalone PINN has the lowest mean frozen SOH MAE (7.76 ± 1.42). The adaptive twin’s value is the later-stream improvement and low update cost, not a claim of the best frozen-cell score.
Adaptive PINN Battery Digital Twin
29 / 31
Notes: Results source: D:/DL/battery_twin/outputs/final_evidence_v2/evidence_results.json and its rendered summaries. The four training epochs are intentionally retained as the executed POC protocol; longer training and broader validation are next experiments.

## Slide 30
PHASE II · EVIDENCE
Adaptation targets, ablations, and robustness results
All required experiment families were executed; the acceptance table is the direct proof-of-concept decision record.
Acceptance measure | Mean ± SD | Target | Status
Post-shift improvement | 80.63 ± 2.46% | ≥ 10% | PASS
Adaptation work ratio | 8.75 ± 0.00% | ≤ 10% | PASS
Prior-domain forgetting | -10.20 ± 4.47% | ≤ 5% | PASS*
Drift events | 7 ± 0 | > 0 | PASS
Scenario | Frozen MAE | Adapted MAE | Events
Clean | 8.81 | 1.73 | 7
V/I/T noise | 9.02 | 1.52 | 7
Missing samples | 8.78 | 1.51 | 7
Sensor drift | 8.88 | 1.69 | 7
Ablation post-shift SOH MAE
Proposed 1.74 · No physics 1.23 · No Transformer 4.09 · No replay 3.97 · No drift detector 1.59 · Full retraining 1.58
Physical checks: SOH bounds 0.00% · negative RUL 0.00% · capacity-curve residual 0.00573 ± 0.00009 · *negative forgetting means prior-domain MAE improved
Adaptive PINN Battery Digital Twin
30 / 31
Notes: Acceptance, ablation, robustness, and physical-validity source: D:/DL/battery_twin/outputs/final_evidence_v2/evidence_results.json. PASS* is interpreted with absolute forgetting magnitude: the measured negative value means the prior-domain error improved rather than degraded.

## Slide 31
PHASE II · EVIDENCE BOUNDARY
What the base review and prior papers actually prove
The project result is new evidence from the executed NASA protocol; literature values remain context because protocols are not directly equivalent.
Source | Experiment / formula focus | Reported result or evidence
0.base_paper.pdf | Methodological review: PINN residuals, electrochemical/ECM/aging/thermal equations, uncertainty, deployment | No single new end-to-end model or one reproducible score; it synthesizes reviewed methods.
Applied Energy paper | Multi-task PINN + simplified Transformer; CV charging features; sensitivity and transfer learning | SOH MAPE 0.75%; degradation-path deviation ≈0.01; RUL MAE 104 cycles in reported cases.
Energy EM-PINN | SEI-layer-growth PDE with PDE, BC, IC, and SOH losses; XJTU/MIT/HUST; six data-volume scenarios | Reported MAPE as low as 0.873%.
Scientific Reports Bat-T-GNN | Cycle-aware patches, time-aware convolution, Transformer, dynamic GNN, PINN-RUL; ablations and corruption tests | Reported NASA values include RMSE 0.014, MAE 0.007, MAPE 0.008; robustness evidence is central.
Complex & Intelligent Systems | PINN + physics-guided augmentation + momentum contrastive learning on B0005/B0006/B0007/B0018 | Compared CNN, BPINN, Informer, XGBoost-ARIMA; added ablation, SHAP, parameter, time, and latency analysis.
Key Contribution
Our core contribution is the integration of drift-triggered replay adaptation with physics-preserving constraints for real-time BMS deployment.
Adaptive PINN Battery Digital Twin
31 / 31
Notes: Sources: D:/DL/0.base_paper.pdf, 1.pdf, 2.pdf, 3.pdf, 4.pdf. External references: Applied Energy https://www.sciencedirect.com/science/article/pii/S0306261925011572; Energy https://www.sciencedirect.com/science/article/pii/S0360544225053964; Scientific Reports https://www.nature.com/articles/s41598-025-28505-5; Complex & Intelligent Systems https://doi.org/10.1007/s40747-025-02194-z. Do not numerically rank the reported values against the project table without harmonizing datasets, labels, splits, and metric definitions.