## Slide 1
SOH · RUL
SCOPE · B.TECH PROJECT
Adaptive Physics-Informed Battery Digital Twin for SOH and RUL Prediction
Energy AI · Battery Management Systems · Physics-Informed Neural Networks
TEAM
M. Chethan Krishna 23BAI0093
K. Shanmukha Santhosh 23BAI0157
Ashok Reddy 23BAI0143

## Slide 2
DOMAIN & MOTIVATION
Project Overview & Use Cases
DOMAIN
Energy AI · Battery Management Systems
TYPE OF DNN
Physics-Informed Neural Network (PINN) + Feedforward DNN
THE CHALLENGE
Li-ion batteries degrade with cycling, temperature and age. Pure deep-learning models need large labeled datasets and can be physically inconsistent; pure physics models are too slow for real-time use.
OUR APPROACH
An Adaptive PINN Battery Digital Twin fuses PINNs, a Transformer Encoder and Incremental Adaptive Learning to continuously estimate SOH and RUL — adapting to new data without full retraining.
WHERE IT APPLIES
Use Case | Impact
Electric Vehicles | Tesla, BYD, Hyundai, Tata EV, MG — predict battery replacement before failure
Battery Swapping Stations | Identify which battery packs should be retired
Solar Energy Storage | Monitor home batteries and predict maintenance
Grid-Scale Storage | Avoid sudden, unplanned battery failures
Drone Batteries | Estimate safe remaining flying time
Space Missions | Battery swaps are impossible — lifetime prediction is critical
Smartphones & Laptops | Sharper degradation estimates than today's health meters
Adaptive PINN Battery Digital Twin
2 / 10

## Slide 3
MOTIVATION
Problem Statement
Lithium-ion batteries power electric vehicles and renewable energy storage, but their performance degrades with charge cycles, temperature, current load and age. Accurately estimating State of Health (SOH) and Remaining Useful Life (RUL) is essential for safety, reliability and efficient maintenance.
Deep Learning Models
Require large volumes of labeled training data
May produce physically inconsistent predictions
Limited generalization to unseen operating conditions
Physics-Based Models
Computationally expensive to run
Difficult to deploy for real-time estimation
Rely on complex electrochemical simulations
Adaptive PINN Battery Digital Twin
3 / 10

## Slide 4
SYSTEM DESIGN
Proposed Approach & Architecture
Real-time sensor data, electrochemical battery physics and deep learning combine to estimate SOH and RUL. The Digital Twin continuously adapts to new battery behaviour through incremental learning — no full retraining required.
1
Historical Battery Dataset
Voltage, current, temperature and cycling history feed the pipeline.
2
Transformer Encoder
Learns long-term degradation patterns across sensor streams.
3
PINN Layer
Embeds electrochemical physics so outputs stay physically consistent.
4
Feedforward NN
Produces final SOH and RUL predictions.
5
Adaptive Learning Module
Detects behaviour shifts and updates the twin incrementally.
Adaptive PINN Battery Digital Twin
4 / 10

## Slide 5
FOUNDATION REFERENCE
Base Paper
Physics-Informed Neural Networks for Battery Modeling and State Estimation: A Methodological Review
Renewable and Sustainable Energy Reviews, 2026
WHY THIS PAPER WAS SELECTED
Comprehensive review of Physics-Informed Neural Networks (PINNs) for battery applications
Covers SOH, RUL, SOC, Digital Twins, thermal diagnosis and internal state reconstruction
Explains multiple methods for embedding battery physics into neural networks
Discusses training stability, domain generalization, uncertainty quantification and interpretability
Lays out future research directions for intelligent Battery Management Systems
Adaptive PINN Battery Digital Twin
5 / 10

## Slide 6
POSITIONING OUR WORK
Literature Review & Research Gap
RESEARCH GAP
Existing PINN models are trained offline, adapt poorly to changing battery behaviour, and remain difficult to deploy in real-time BMS. Lightweight, continual-learning methods are still an open problem.
Paper | Key Contribution | Limitation | Our Improvement
Applied Energy (2025) | PINN + Transformer + multi-task learning predicts SOH, RUL and degradation path | Offline training; adapting to new behaviour needs retraining | Adaptive Digital Twin with incremental fine-tuning
Energy (2026) | EM-PINN integrates SEI growth physics for accurate SOH estimation | SOH-only; no Digital Twin or continual adaptation | Combines PINN with a Digital Twin predicting SOH and RUL
Scientific Reports (2025) | Cycle-aware physics-informed framework for RUL prediction | Offline; limited personalization per battery | Continuously updates predictions with new operational data
Complex & Intelligent Systems (2025) | PINN + contrastive learning for low-label SOH estimation | Train-then-deploy workflow; no post-deployment adaptation | Supports incremental learning without full retraining
Proposed Work | Transformer + PINN + Feedforward DNN + Digital Twin + Adaptive Learning | — | Incremental fine-tuning on new battery behaviour, preserving physics constraints
Adaptive PINN Battery Digital Twin
6 / 10

## Slide 7
FOUNDATION FOR TRAINING
Datasets Used & Rationale
SELECTED DATASETS
Public benchmark battery datasets cited across the reviewed papers, spanning lab-aged, second-life, and vehicle-field conditions, chosen to validate SOH/RUL estimation under diverse chemistries and operating regimes.
Dataset | Scope | Link | Why This Dataset
NASA & Oxford Battery | Lab-aged Li-ion cells; narrow current/temperature range; classic PINN-SOH benchmark | data.nasa.gov (PCoE) / howey-lab Oxford Battery Degradation Dataset | [0] Standard reference set used by our base-paper PINN methodology review to validate degradation-physics constraints
Stanford-MIT-Toyota (Severson) | 124 LFP/graphite cells, 72 fast-charging policies, cycled to end-of-life | data.matr.io (Battery Evaluation and Early Prediction project) | [1] Used by the RUL-focused papers for early-cycle degradation trajectories and fast-charging diversity
TJU & XJTU | Multi-chemistry aging data with IC-curve health features across varied cycling protocols | Tianjin University / Xi'an Jiaotong University battery aging repositories | [2] Referenced by the time-series PINN-SOH literature to test cross-dataset transfer of the Adaptive Learning module
CALCE & Panasonic 18650PF | Dynamic charge/discharge cycles, -10°C to 20°C, multi-temperature conditions | calce.umd.edu (Battery Research Group) / NASA Ames Prognostics Center | [3] Provides low-temperature, condition-diverse cycles to stress-test physics-informed robustness
Second-Life LIB (SL-LIB) | 84 retired batteries, 21 working conditions, real second-life usage patterns | Self-designed dataset (Bayesian PINN, Applied Energy 2025) | [4] Real-world retired-battery data supports validating adaptive learning on genuinely shifting degradation behaviour
Datasets Used & Rationale
7 / 11

## Slide 8
WHAT SETS THIS WORK APART
Novel Contribution: Adaptive Incremental Learning
Traditional models are trained once on historical data. When battery behaviour shifts with aging, temperature or charging patterns, the whole model must often be retrained — expensive and impractical for real-time BMS.
WITHOUT ADAPTIVE LEARNING
Old + New
Dataset
Retrain
Everything
Deploy New
Model
WITH ADAPTIVE LEARNING (PROPOSED)
Existing Model
+ New Data
Fine-Tune
Only
Updated
Model
HOW IT WORKS
1
Monitor real-time sensor data (V, I, temperature, SOC, cycle count)
2
Detect changes in degradation behaviour
3
Store important new data in a replay buffer
4
Incrementally fine-tune the existing model
5
Update the Digital Twin — no full retraining
ADVANTAGES
Eliminates full model retraining
Adapts to changing battery behaviour
Personalized prediction per battery
Physics-consistent predictions via PINN
Fit for real-time BMS deployment
Adaptive PINN Battery Digital Twin
8 / 11

## Slide 9
REAL-WORLD IMPACT
Applications
1
Electric Vehicles
Predict battery replacement before failure occurs.
2
Solar Storage
Monitor home batteries and predict maintenance needs.
3
Smart Grids
Avoid sudden, costly battery failures at scale.
4
Drones
Estimate safe remaining flying time in-flight.
5
Laptops & Smartphones
More accurate battery degradation estimates.
Adaptive PINN Battery Digital Twin
9 / 11

## Slide 10
CONCLUSION
Project Summary
Proposed an Adaptive Physics-Informed Battery Digital Twin for accurate SOH and RUL estimation.
Integrated Transformer Encoder, PINN and Feedforward DNN to combine data-driven learning with battery physics.
Introduced incremental adaptive learning to keep the Digital Twin current without full model retraining.
Overcomes key limits of pure deep-learning and pure physics-based models with real-time, physically consistent predictions.
Potential impact: Electric Vehicles, Battery Management Systems, Renewable Energy Storage, Smart Grids, Drones and Consumer Electronics.
Adaptive PINN Battery Digital Twin
10 / 11
Adaptive PINN Battery Digital Twin
9 / 10

## Slide 11
SOURCES
References
1
Physics-informed neural networks for battery modeling and state estimation: A methodological review
Renewable and Sustainable Energy Reviews, 2026 https://www.sciencedirect.com/science/article/pii/S1364032126005253
2
Physics-informed neural network for co-estimation of state of health, remaining useful life, and short-term degradation path in Lithium-ion batteries
Applied Energy, 2025 https://www.sciencedirect.com/science/article/pii/S0306261925011572
3
Physical informed neural network for SOH estimation of Lithium-ion battery with electrochemical mechanism
Energy, 2026 https://www.sciencedirect.com/science/article/pii/S0360544225053964
4
A cycle-aware and physics-informed framework for battery remaining useful life prediction
Scientific Reports, 2025 https://www.researchgate.net/publication/399255851_A_cycle-aware_and_physics-informed_framework_for_battery_remaining_useful_life_prediction
5
Physics-informed neural network and momentum contrastive learning for battery state of health estimation
Complex & Intelligent Systems, 2025 https://www.researchgate.net/publication/398786756_Physics-informed_neural_network_and_momentum_contrastive_learning_for_battery_state_of_health_estimation
Adaptive PINN Battery Digital Twin
11 / 11