## Slide 1
SOH · RUL
SCOPE · B.TECH PROJECT
Adaptive Physics-Informed Battery Digital Twin for SOH and RUL Prediction
Energy AI · Battery Management Systems · Physics-Informed Neural Networks
TEAM
M. Chethan Krishna 23BAI0093
K. Shanmukha Santhosh 23BAI0157
Ashok Reddy 23BAI0143

## Slide 2
DOMAIN & MOTIVATION
Project Overview & Use Cases
DOMAIN
Energy AI · Battery Management Systems
TYPE OF DNN
Physics-Informed Neural Network (PINN) + Feedforward DNN
THE CHALLENGE
Li-ion batteries degrade with cycling, temperature and age. Pure deep-learning models need large labeled datasets and can be physically inconsistent; pure physics models are too slow for real-time use.
OUR APPROACH
An Adaptive PINN Battery Digital Twin fuses PINNs, a Transformer Encoder and Incremental Adaptive Learning to continuously estimate SOH and RUL — adapting to new data without full retraining.
WHERE IT APPLIES
Use Case | Impact
Electric Vehicles | Tesla, BYD, Hyundai, Tata EV, MG — predict battery replacement before failure
Battery Swapping Stations | Identify which battery packs should be retired
Solar Energy Storage | Monitor home batteries and predict maintenance
Grid-Scale Storage | Avoid sudden, unplanned battery failures
Drone Batteries | Estimate safe remaining flying time
Space Missions | Battery swaps are impossible — lifetime prediction is critical
Smartphones & Laptops | Sharper degradation estimates than today's health meters
Adaptive PINN Battery Digital Twin
2 / 10

## Slide 3
MOTIVATION
Problem Statement
Lithium-ion batteries power electric vehicles and renewable energy storage, but their performance degrades with charge cycles, temperature, current load and age. Accurately estimating State of Health (SOH) and Remaining Useful Life (RUL) is essential for safety, reliability and efficient maintenance.
Deep Learning Models
Require large volumes of labeled training data
May produce physically inconsistent predictions
Limited generalization to unseen operating conditions
Physics-Based Models
Computationally expensive to run
Difficult to deploy for real-time estimation
Rely on complex electrochemical simulations
Adaptive PINN Battery Digital Twin
3 / 10

## Slide 4
SYSTEM DESIGN
Proposed Approach & Architecture
Real-time sensor data, electrochemical battery physics and deep learning combine to estimate SOH and RUL. The Digital Twin continuously adapts to new battery behaviour through incremental learning — no full retraining required.
1
Historical Battery Dataset
Voltage, current, temperature and cycling history feed the pipeline.
2
Transformer Encoder
Learns long-term degradation patterns across sensor streams.
3
PINN Layer
Embeds electrochemical physics so outputs stay physically consistent.
4
Feedforward NN
Produces final SOH and RUL predictions.
5
Adaptive Learning Module
Detects behaviour shifts and updates the twin incrementally.
Adaptive PINN Battery Digital Twin
4 / 10

## Slide 5
FOUNDATION REFERENCE
Base Paper
Physics-Informed Neural Networks for Battery Modeling and State Estimation: A Methodological Review
Renewable and Sustainable Energy Reviews, 2026
WHY THIS PAPER WAS SELECTED
Comprehensive review of Physics-Informed Neural Networks (PINNs) for battery applications
Covers SOH, RUL, SOC, Digital Twins, thermal diagnosis and internal state reconstruction
Explains multiple methods for embedding battery physics into neural networks
Discusses training stability, domain generalization, uncertainty quantification and interpretability
Lays out future research directions for intelligent Battery Management Systems
Adaptive PINN Battery Digital Twin
5 / 10

## Slide 6
POSITIONING OUR WORK
Literature Review & Research Gap
RESEARCH GAP
Existing PINN models are trained offline, adapt poorly to changing battery behaviour, and remain difficult to deploy in real-time BMS. Lightweight, continual-learning methods are still an open problem.
Paper | Key Contribution | Limitation | Our Improvement
Applied Energy (2025) | PINN + Transformer + multi-task learning predicts SOH, RUL and degradation path | Offline training; adapting to new behaviour needs retraining | Adaptive Digital Twin with incremental fine-tuning
Energy (2026) | EM-PINN integrates SEI growth physics for accurate SOH estimation | SOH-only; no Digital Twin or continual adaptation | Combines PINN with a Digital Twin predicting SOH and RUL
Scientific Reports (2025) | Cycle-aware physics-informed framework for RUL prediction | Offline; limited personalization per battery | Continuously updates predictions with new operational data
Complex & Intelligent Systems (2025) | PINN + contrastive learning for low-label SOH estimation | Train-then-deploy workflow; no post-deployment adaptation | Supports incremental learning without full retraining
Proposed Work | Transformer + PINN + Feedforward DNN + Digital Twin + Adaptive Learning | — | Incremental fine-tuning on new battery behaviour, preserving physics constraints
Adaptive PINN Battery Digital Twin
6 / 10

## Slide 7
FOUNDATION FOR TRAINING
Datasets Used & Rationale
SELECTED DATASETS
Public benchmark battery datasets cited across the reviewed papers, spanning lab-aged, second-life, and vehicle-field conditions, chosen to validate SOH/RUL estimation under diverse chemistries and operating regimes.
Dataset | Scope | Link | Why This Dataset
NASA & Oxford Battery | Lab-aged Li-ion cells; narrow current/temperature range; classic PINN-SOH benchmark | data.nasa.gov (PCoE) / howey-lab Oxford Battery Degradation Dataset | [0] Standard reference set used by our base-paper PINN methodology review to validate degradation-physics constraints
Stanford-MIT-Toyota (Severson) | 124 LFP/graphite cells, 72 fast-charging policies, cycled to end-of-life | data.matr.io (Battery Evaluation and Early Prediction project) | [1] Used by the RUL-focused papers for early-cycle degradation trajectories and fast-charging diversity
TJU & XJTU | Multi-chemistry aging data with IC-curve health features across varied cycling protocols | Tianjin University / Xi'an Jiaotong University battery aging repositories | [2] Referenced by the time-series PINN-SOH literature to test cross-dataset transfer of the Adaptive Learning module
CALCE & Panasonic 18650PF | Dynamic charge/discharge cycles, -10°C to 20°C, multi-temperature conditions | calce.umd.edu (Battery Research Group) / NASA Ames Prognostics Center | [3] Provides low-temperature, condition-diverse cycles to stress-test physics-informed robustness
Second-Life LIB (SL-LIB) | 84 retired batteries, 21 working conditions, real second-life usage patterns | Self-designed dataset (Bayesian PINN, Applied Energy 2025) | [4] Real-world retired-battery data supports validating adaptive learning on genuinely shifting degradation behaviour
Datasets Used & Rationale
7 / 11

## Slide 8
WHAT SETS THIS WORK APART
Novel Contribution: Adaptive Incremental Learning
Traditional models are trained once on historical data. When battery behaviour shifts with aging, temperature or charging patterns, the whole model must often be retrained — expensive and impractical for real-time BMS.
WITHOUT ADAPTIVE LEARNING
Old + New
Dataset
Retrain
Everything
Deploy New
Model
WITH ADAPTIVE LEARNING (PROPOSED)
Existing Model
+ New Data
Fine-Tune
Only
Updated
Model
HOW IT WORKS
1
Monitor real-time sensor data (V, I, temperature, SOC, cycle count)
2
Detect changes in degradation behaviour
3
Store important new data in a replay buffer
4
Incrementally fine-tune the existing model
5
Update the Digital Twin — no full retraining
ADVANTAGES
Eliminates full model retraining
Adapts to changing battery behaviour
Personalized prediction per battery
Physics-consistent predictions via PINN
Fit for real-time BMS deployment
Adaptive PINN Battery Digital Twin
8 / 11

## Slide 9
REAL-WORLD IMPACT
Applications
1
Electric Vehicles
Predict battery replacement before failure occurs.
2
Solar Storage
Monitor home batteries and predict maintenance needs.
3
Smart Grids
Avoid sudden, costly battery failures at scale.
4
Drones
Estimate safe remaining flying time in-flight.
5
Laptops & Smartphones
More accurate battery degradation estimates.
Adaptive PINN Battery Digital Twin
9 / 11

## Slide 10
CONCLUSION
Project Summary
Proposed an Adaptive Physics-Informed Battery Digital Twin for accurate SOH and RUL estimation.
Integrated Transformer Encoder, PINN and Feedforward DNN to combine data-driven learning with battery physics.
Introduced incremental adaptive learning to keep the Digital Twin current without full model retraining.
Overcomes key limits of pure deep-learning and pure physics-based models with real-time, physically consistent predictions.
Potential impact: Electric Vehicles, Battery Management Systems, Renewable Energy Storage, Smart Grids, Drones and Consumer Electronics.
Adaptive PINN Battery Digital Twin
10 / 11
Adaptive PINN Battery Digital Twin
9 / 10

## Slide 11
SOURCES
References
1
Physics-informed neural networks for battery modeling and state estimation: A methodological review
Renewable and Sustainable Energy Reviews, 2026 https://www.sciencedirect.com/science/article/pii/S1364032126005253
2
Physics-informed neural network for co-estimation of state of health, remaining useful life, and short-term degradation path in Lithium-ion batteries
Applied Energy, 2025 https://www.sciencedirect.com/science/article/pii/S0306261925011572
3
Physical informed neural network for SOH estimation of Lithium-ion battery with electrochemical mechanism
Energy, 2026 https://www.sciencedirect.com/science/article/pii/S0360544225053964
4
A cycle-aware and physics-informed framework for battery remaining useful life prediction
Scientific Reports, 2025 https://www.researchgate.net/publication/399255851_A_cycle-aware_and_physics-informed_framework_for_battery_remaining_useful_life_prediction
5
Physics-informed neural network and momentum contrastive learning for battery state of health estimation
Complex & Intelligent Systems, 2025 https://www.researchgate.net/publication/398786756_Physics-informed_neural_network_and_momentum_contrastive_learning_for_battery_state_of_health_estimation
Adaptive PINN Battery Digital Twin
11 / 11

## Slide 12
PHASE II · REVIEW 2
Model Design & Experimental Study
Completed implementation, evaluation evidence, and faculty-ready proof of concept
NASA-first evidence bundle
54 hyperparameter combinations · 3 random seeds · 18 ablation rows · 12 robustness rows
Course rubric focus
Model architecture · Multiple models · Hyperparameter tuning · Experimental analysis · Presentation and AI reflection
Adaptive PINN Battery Digital Twin
12 / 21
Notes: Phase II section appended to the supplied deck. Evidence source: D:/DL/battery_twin/outputs/final_evidence_v2/evidence_results.json.

## Slide 13
PHASE II · DELIVERABLE
The project moved from proposal to tested prototype
The original deck described the direction. This section records the executable implementation and measured evidence.
1
Data contract
NASA B0005, B0006, B0007, and B0018 are parsed into ordered discharge-cycle records with voltage, current, temperature, time-gap, and capacity.
2
Model stack
DNN, GRU, Transformer-only, PINN, and adaptive Transformer-plus-physics models run under the same held-out-cell protocol.
3
Online learning
A drift detector triggers low-cost replay-buffer updates as the held-out stream arrives in time order.
4
Faculty evidence
The run exports final comparison tables, ablations, robustness results, physical diagnostics, figures, and a reflection script.
5
What remains a proposal
SEI-PDE physics and broad multi-chemistry validation remain extensions because the NASA POC does not expose every required electrochemical variable.
6
Evidence discipline
Reported paper metrics stay separate from new project metrics. The project claims only what the executed protocol measures.
Adaptive PINN Battery Digital Twin
13 / 21
Notes: Project implementation files: D:/DL/battery_twin/src/battery_twin and D:/DL/battery_twin/scripts. The source audit in the HTML report distinguishes proposal claims, literature evidence, and new student evidence.

## Slide 14
PHASE II · DATASET
NASA cells and a leakage-safe evaluation protocol
The official NASA PCoE repository provides the first committed dataset for this proof of concept.
Item | Project choice | Why it matters
Cells | B0005 / B0006 / B0007 train · B0018 held out | Battery-level separation tests transfer to a new cell.
Labels | SOH = capacity / nominal capacity × 100 · EOL = 70% SOH | RUL = EOL cycle − current cycle.
Inputs | Voltage · current · temperature · delta_t · cycle index | Measured timing is retained with masks.
Protocol | 504 train windows · 132 test windows · 33 initial · 99 stream | Later cycles arrive sequentially for adaptation.
Seeds | 7 · 17 · 27 | Final tables report mean ± standard deviation.
EOL RULE
70% SOH
HELD-OUT CELL
B0018
CYCLES PARSED
636 total
ORDER
Time-aware
METRIC UNIT
RUL in cycles
Adaptive PINN Battery Digital Twin
14 / 21
Notes: Dataset source: https://www.nasa.gov/intelligent-systems-division/discovery-and-systems-health/pcoe/pcoe-data-set-repository/. Local audit and labels are implemented in data.py and features.py. The 636-cycle count is the parser audit across the four selected NASA files.

## Slide 15
PHASE II · ARCHITECTURE
From measured cycle to adaptive digital-twin state
The first-stage physics model uses relationships supported by the NASA measurements.
•
NASA records
Cycle-level voltage, current, temperature, time, capacity
•
Masked encoder
Measured points + delta_t, no blind interpolation
•
Temporal model
History across cycles with Transformer context
•
SOH / RUL heads
Bounded SOH 0–100 and non-negative RUL
•
Physics losses
Soft degradation, RUL order, capacity-curve residual
•
Replay adaptation
Drift trigger, recent + representative history
Training objective
L_total = L_data + λ_phys L_phys + λ_cons L_cons
The SEI-growth PDE formulation remains a Stage 2 extension until every variable and parameter is available and verified.
Adaptive PINN Battery Digital Twin
15 / 21
Notes: Implementation sources: models.py, physics.py, training.py. The methodology review and EM-PINN paper inform the physics discussion, but the student POC does not claim to reproduce the SEI-PDE experiment.

## Slide 16
PHASE II · TUNING
The selected configuration came from the complete grid
Every requested combination ran across seeds 7, 17, and 27 before the final evidence pass.
Grid dimension | Values tested
Hidden size | 64 · 128
Learning rate | 0.0001 · 0.0005 · 0.001
Physics weight | 0.1 · 1 · 10
Replay size | 128 · 512 · 2048
Total combinations | 54 × 3 seeds = 162 runs
Selected configuration
Hidden size 64
Learning rate 0.001
Physics weight 0.1
Replay size 128
The final evidence runner then used the selected configuration on the full default cycle-window representation.
GRID STATUS
54 / 54 complete
MODEL COUNT
5 comparisons
EVIDENCE MODE
Held-out cell
OUTPUT
JSON + CSV + PNG
Adaptive PINN Battery Digital Twin
16 / 21
Notes: Tuning source: D:/DL/battery_twin/outputs/tuning/grid.json. The grid JSON records combinations_requested = 54, combinations_run = 54, and seeds = [7, 17, 27].

## Slide 17
PHASE II · MODEL COMPARISON
The standalone PINN led frozen SOH accuracy
All model rows use the same B0018 held-out evaluation protocol and four training epochs.
Model | SOH MAE | RUL MAE (cycles) | SOH R²
DNN | 11.05 ± 0.25 | 37.04 ± 6.18 | -6.43
GRU | 10.52 ± 1.03 | 36.39 ± 4.95 | -1.87
Transformer-only | 11.50 ± 0.56 | 43.98 ± 9.94 | -6.57
PINN without adaptation | 7.76 ± 1.42 | 38.15 ± 4.59 | -3.86
Adaptive twin | 10.05 ± 1.46 | 38.36 ± 3.39 | -4.48
Adaptive twin
10.05 ± 1.46 SOH MAE · 38.36 ± 3.39 RUL MAE
Best frozen SOH row
PINN: 7.76 ± 1.42 SOH MAE
Adaptive PINN Battery Digital Twin
17 / 21
Notes: Metrics source: D:/DL/battery_twin/outputs/final_evidence_v2/evidence_results.json and final_summary.csv. Paper metrics are not numerically ranked against this table because datasets, splits, labels, and metric scales differ.

## Slide 18
PHASE II · ABLATIONS
Replay adaptation delivered the low-cost online update
The ablation table shows which components mattered in the ordered B0018 stream.
Variant | Post-shift SOH MAE | Improvement | Work | Events
Proposed adaptive | 1.74 | 80.63% | 8.75% | 7
No physics | 1.23 | 86.98% | 8.75% | 7
No Transformer | 4.09 | 50.39% | 8.75% | 7
No replay | 3.97 | 53.23% | 8.75% | 7
No drift detection | 1.59 | 81.91% | 15.00% | 12
Full retraining | 1.58 | Reference | 100.00% | —
TARGET 1
80.63% improvement
TARGET 2
8.75% work
TARGET 3
−10.20% forgetting
DETECTOR
7 updates / seed
Adaptive PINN Battery Digital Twin
18 / 21
Notes: Ablation source: evidence_results.json and ablation_summary.csv. Negative forgetting means the initial-domain SOH MAE improved after adaptation. Full retraining is the cost reference.

## Slide 19
PHASE II · ROBUSTNESS
The adaptive state remained useful under sensor corruption
Robustness scenarios use the same trained proposal and corrupt the ordered stream before adaptation.
Scenario | Frozen SOH MAE | Adaptive SOH MAE | Updates
Clean ordered stream | 8.81 | 1.73 | 7
Voltage/current/temp noise | 9.02 | 1.52 | 7
10% missing samples | 8.78 | 1.51 | 7
Sensor drift | 8.88 | 1.69 | 7
Diagnostic | Mean ± SD
SOH bounds violations | 0.00%
Negative RUL | 0.00%
SOH degradation violation | 21.43%
SOH/RUL consistency violation | 30.95%
Capacity-curve residual | 0.00573
Interpretation
Hard bounds stayed at zero. Soft monotonic diagnostics stayed nonzero, so the result supports a measured proof of concept with calibration limits rather than perfect electrochemical validity.
Adaptive PINN Battery Digital Twin
19 / 21
Notes: Robustness and physical-validity source: evidence_results.json. The monotonic rates are diagnostics because real cells can show local capacity regeneration. Capacity-curve residual is the first-stage data-supported residual, not an SEI-PDE residual.

## Slide 20
PHASE II · FACULTY EVIDENCE
Proof of experiment mapped to the course rubric
The deck now points to concrete artifacts a reviewer can inspect.
Rubric criterion | What to show | Artifact
Model architecture design | Data → masked encoder → temporal model → physics losses → heads → replay update | HTML report · Section 05
Multiple models | DNN, GRU, Transformer-only, PINN, adaptive twin | final_summary.csv
Hyperparameter tuning | 54 combinations across three seeds | tuning/grid.json
Experimental analysis | Ablations, robustness, physical checks, acceptance table | evidence_results.json + PNG figures
Presentation and reflection | 6-minute walkthrough and AI pair-programming reflection | video_reflection_script.md
Recording checklist
Show the design diagram · show all five models · open the 54-combination grid · show one ablation and one robustness figure · read PASS status exactly
Adaptive PINN Battery Digital Twin
20 / 21
Notes: Faculty rubric source: D:/DL/RUBRICS FOR COURSE BASED DESIGN PROJECT - FALL 26-27.pdf and the supplied Phase II screenshots. The actual recording must be made and uploaded by the student; this slide and video_reflection_script.md prepare the evidence.

## Slide 21
PHASE II · FINAL STATUS
A tested adaptive POC with a clear next experiment
The strongest evidence is the low-cost online update. The main limitation is the small four-cell dataset.
What the run supports
1
Adaptation benefit
80.63% lower post-shift SOH MAE than frozen.
2
Low update cost
8.75% of full-retraining work.
What the run does not prove
• Universal chemistry or temperature generalization
• Perfect monotonic degradation behavior
• SEI-PDE validity without additional variables
• A direct numerical ranking against the four papers
Next experiment
Calibrate physics weights, add longer training, and repeat leave-one-cell-out validation before making a broader scientific claim.
Adaptive PINN Battery Digital Twin
21 / 21
Notes: Closing reflection: AI helped translate the proposal and rubric into code, tests, and evidence tables. Human scientific judgment kept unsupported SEI-PDE claims out of the first NASA implementation. Manual video recording remains the only presentation step not automated here.